## Slide 1: Sensors, Microcontrollers & Packet Tracer
Frank Walsh

## Slide 2: Agenda
Main aim is to provide enough knowledge so we can build sensor/actuator systems using a Microcontroller
  Can simulate this in PacketTracer for now
Sensors/Transducers
Sensor Types
Connecting to a Microcontroller
Sensors in Packet Tracer

## Slide 3: Context: Physical Computing
Break away from conventional input/output peripherals:
  Keyboard, mouse, screen
Think about how human/environment signals can be captured and changed into electronic signals that can be interpreted by a computing device.
Physical computing applications tend to depend on people for input (and sometimes output), and transform that input into another form, like an animation, a sound, or motion.
Sometimes powerfully fuses art and technology.

## Slide 4: Electricity 101: Ohms Law
Voltage (V), Current (I), and Resistance (R) are all related, by the following formula:
V = I x R
electrical power (P) (measured in watts), as follows:
Watts = Volts * Amps
P = V * I

## Slide 5: Electricity 101: Circuits
Series & Parallel Circuits

## Slide 6: What are Sensors
Transducer
  a device that converts a primary form of energy into a corresponding signal with a different energy form
  Primary Energy Forms: mechanical, thermal, electromagnetic, optical, chemical, etc.
  Can be a sensor or an actuator
A Sensor is a device that detects/measures a signal/stimulus
  Acquires data from the “real world”
An Actuator generates a signal or stimulus from electrical signal.
  Example: Servo Motor.
Sensors are everywhere
  In our bodies, automobiles, airplanes, cellular telephones, radios
  Necessary for automation.

## Slide 7: Sensor Systems
Typically interested in electronic sensors
  convert desired parameter into electrically measurable signal
A Sensor may include:
  primary transducer: changes “real world” parameter into electrical signal
  secondary transducer: converts electrical signal into analog or digital values
Simple Electronic Sensor System:

## Slide 8: Detectable Phenomena

## Slide 9: Sensor Use: Project Examples

## Slide 10: Temperature Sensors
Temperature sensors appear in building, chemical process plants, engines, appliances, computers, and many other devices that require temperature monitoring
Many physical phenomena depend on temperature, so we can often measure temperature indirectly by measuring pressure, volume, electrical resistance, and strain
Type of common temperature transducer
  Resistance Temperature Detector (RTD)
  Thermistors
  Thermocouples

## Slide 11: Thermistor
A thermistor is a type of resistor with resistance varying according to its temperature. The resistance is measured by passing a small, measured direct current through it and measuring the voltage drop produced.

## Slide 12: Optical Encoders
Notes: A rotary encoder, also called a shaft encoder, is an electro-mechanical device that converts the angular position or motion of a shaft or axle to analog or digital output signals.
Incremenntal Encoders, absolute encoders
he output of an absolute encoder indicates the current shaft position, making it an angle transducer. The output of an incremental encoder provides information about the motion of the shaft, which typically is processed elsewhere into information such as position, speed and distance.

## Slide 13: Sample Problem: Sensor Analysis
How far does vehicle travel for 1 encoder count?
How many counts are there per meter of travel?
What should the wheel diameter be for 1cm / count.

## Slide 14: Sample Problem: How far does vehicle travel for 1 encoder count?

## Slide 15: Sample Problem: How many encoder counts will there be for 1 meter of travel?

## Slide 16: Sample Problem: Suppose I want 1.0 cm / count, what wheel diameter

## Slide 17: Potentiometer

## Slide 18: Band Sensor

## Slide 19: Force Sensor
Detect and measure a relative change in force or applied load
Detect and measure the rate of change in force
Identify force thresholds and trigger appropriate action
Detect contact and/or touch
Applications:
  Touch Pads (i.e. VR Gloves, Joysticks)
  Alarm Systems
  Aerospace
  Robotic Grip Force

## Slide 20: Accelerometers
Measures Acceleration
Application:
  Vibrations, blasts, impacts, shock waves
  Air bags, washing machines, car alarm
They can come in 1, 2 or 3 axis configurations
  With 3 axis it gives a vector of the accelerations direction (after accounting for gravity)
Used in electronics like the Wii and iPhone for user input

## Slide 21: Light Sensor
  photoconductor
    light  R
  photodiode
    light  I

## Slide 22: Connecting Sensors to Microcontroller/Single Board Computer
Analog Sensors
  many microcontrollers have a built-in ADC
    8-bit to 12-bit resolution common
    many have multi-channel ADC inputs
Digital Sensors
  serial I/O
    use serial I/O port, store data in memory to analyze later
    Synchronous (with clock)
      must match byte format, stop/start bits, parity check, etc.
    asynchronous (no clock): more common for communication
      must match baud rate and bit width, transmission protocol, etc.
µC
signal timing
memory
keypad
sensor
sensor
display
instrument

## Slide 23: “Smart” Sensors
“Smart sensor” = sensor with built-in signal processing & communication
  E.g., combining a “dumb sensor” and a microcontroller
Data Acquisition Cards (DAQ)
  PC card with analog and digital I/O
  interface through LabVIEW or user-generated code
Communication Links Common for Sensors
  asynchronous serial communication
    universal asynchronous receive and transmit (UART)
      1 receive line + 1 transmit line. nodes must match baud rate & protocol
    RS232 Serial Port on PCs uses UART format (but at +/- 12V)
    can buy a chip to convert from UART to RS232
  synchronous serial comm.
    serial peripheral interface (SPI)
      1 clock + 1 bidirectional data + 1 chip select/enable
    I2C = Inter Integrated Circuit bus
      designed by Philips for comm. inside TVs, used in several commercial sensor systems
    IEEE P1451: Sensor Comm. Standard
      several different sensor comm. protocols for different applications

## Slide 24: Sensor Calibration
Sensors can exhibit non-ideal effects
  offset: nominal output ≠ nominal parameter value
  nonlinearity: output not linear with parameter changes
  cross parameter sensitivity: secondary output variation with, e.g., temperature
Calibration - adjusting output to match parameter
  analog signal conditioning
  look-up table
  digital calibration
    T = a + bV +cV2,
      T= temperature; V=sensor voltage;
      a,b,c = calibration coefficients
Compensation
  remove secondary sensitivities
  must have sensitivities characterized
  can remove with polynomial evaluation
    P = a + bV + cT + dVT + e V2, where P=pressure, T=temperature

## Slide 25: Sensor Performance
Range
  maximum and minimum values that can be measured
Resolution or discrimination
  smallest discernible change in the measured value
Error
  difference between the measured and actual values
    random errors
    systematic errors
Accuracy, inaccuracy, uncertainty
  accuracy is a measure of the maximum expected error
Linearity
  maximum deviation from a ‘straight-line’ response
Sensitivity
  a measure of the change produced at the output for a given change in the quantity being measured

## Slide 26: Sensor Performance
Precision/Accuracy
  a measure of the lack of random errors (scatter)

## Slide 27: Packet Tracer 8.x and IoT
Packet Tracer 8.x can be used as a prototyping tool.
There is a new group icon contained in Packet Tracer that is labeled Components.
The PT IoT boards contains an MCU and a SBC.
The MCU and SBC are similar to an Arduino and a Raspberry Pi, respectively.
There are also actuators and sensors that can be used in prototypes.
The IoE Custom Cable found in the Connections group can be used to connect IoT things to an MCU board.

## Slide 28: Packet Tracer Demo….