## Slide 1: Physical Computing

## Slide 2: Agenda
Physical Computing
Electricity and Circuits 101
Electronic Components
Programming with the GPIO
Lab Scenario (SMTP)
PiCamera – Images and Streaming

## Slide 3: Physical Computing
“A creative framework for understanding human beings' relationship to the world”

## Slide 4: Physical Computing
Break away from conventional input/output peripherals:
  Keyboard, mouse, touch screen
Think about how human/environment signals can be captured and changed into electronic signals that can be interpreted by a computing device.
Physical computing applications tend to depend on people for input (and sometimes output), and transform that input into another form, like an animation, a sound, or motion.
Sometimes powerfully fuses art and technology.
Notes: I’m very functional about it – mousetrap that texts you when it’s been activated. Control my brewing from work. Emencly imprssic when fused with art and creativity
Up to now – celectrical omponents contained in devices. Now out in the open
Need to know something about Electricity

## Slide 5: Electricity
Electricity is the flow of electrical energy through some conductive material.
Sensors are components that convert other forms of energy into electrical energy so we can read the changes in those other forms.
  Transduction (e.g. microphone)
Voltage is a measure of the difference in electrical potential energy between two points in a circuit. It is measured in Volts.
Current is a measure of the magnitude of the flow of electrons through a particular point in a circuit. It is measured in Amperes, or Amps.
Resistance is a measure of a material’s ability to oppose the flow of electricity. It is measured in Ohms.
Notes: Imagine an avalanche of snow on a mountain. The height of the mountain is analogous to the voltage; the higher the mountain, the more potential energy the falling material has. The amount of snow and rocks in the avalanche is analogous to the current. And the steepness of the mountain is analogous to the resistance: the steeper the mountain, the less it will resist the flow of the snow and rocks. We’ll define this a bit more formally below.

## Slide 6: Electricity: Relationship
Voltage (V), Current (I), and Resistance (R) are all related, by the following formula:
V = I x R
electrical power (P) (measured in watts), as follows:
Watts = Volts * Amps
P = V * I

## Slide 7: Circuits 1
Physical Computing usually involves interfacing a computing device with electrical circuit(s).
A circuit needs a:
  Electrical Energy Source (e.g. battery)
  Load (Converts elec energy to something else)
Notes: The reason we want to build circuits is to make electricity do useful things for us. The way we do that is by putting things in the circuit that use the current flow to light up, make noise, run programs, etc.
These things are called loads, The same way you could be loaded down with too much weight, it’s possible to load down a power supply too much, which will slow down the current flow. But unlike you, it’s also possible to load down a circuit too little - this may let too much current flow (imagine running too fast if you weren’t carrying any weight), which can burn out your parts or even the power supply.

## Slide 8: Circuits 2
Electricity needs to flow to do anything useful.
  Needs a path to flow through, which must be an electrical conductor(like copper)
Electricity(Current) will flow from a higher voltage(+) to a lower voltage(-) or ground.
Notes: Short Circuit: if you DON'T put anything in to restrict the current flow, there won't be anything to slow down the current, and it will try to be infinite! Can cause our wire to burn up, damage the power supply, drain your battery, or other exciting thing.
Too much current: A closely related problem is accidentally letting too much current flow through part of your circuit, causing a part to burn up. This isn't quite a short circuit, but it's close. This most often happens when you use the incorrect resistor value, which lets too much current flow through another component such as an LED.
Open Circuit: The opposite of a short circuit is an open circuit. This is a circuit where the loop isn't fully connected (and therefore this isn't really a circuit at all). If your circuit doesn't work, the most likely cause is an open circuit. This is usually due to a broken connection or a loose wire. (Short circuits can steal all the power from the rest of your circuit, so be sure to look for those as well.)

## Slide 9: Electronic Components
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 10: Electronics: Breadboard
Used for prototyping electronic solutions
Notes: Terminal Strips: You can see lots of parallel rows of metal strips on the bottom of the breadboard. If you insert a component into hole, it’ll be connected to anything else placed in that row( a bit like a socket. This is because the metal rows are conductive and allow current to flow from any point in that strip.
Each row is separated by a ravine in the middle of the breadboard. This ravine isolates both sides of a given row from one another, and they are not electrically connected. Each side of a given row is disconnected from the other, leaving you with five spots for components on either side.
POWER RAILS: breadboards usually have what are called power rails that run along the sides. The metal strips that are identical to the ones in the middle , except they run the fill length of the board. When building a circuit, you tend to need power in lots of different places. The power rails give you lots of easy access to power wherever you need it in your circuit. Usually they will be labeled with a ‘+’ and a ‘-’ and have a red and blue or black stripe, to indicate the positive and negative side.
Your breadboard will have numbers and letters marked on various rows and columns. Circuits can get complicated so this helps guide you when building your circuit

## Slide 11: LEDs
Emits light when current passes through
Typical LED requires 2V at 20mA
RGB LEDs, LED strips, IR LEDs, Ultrabright
This Photo by Unknown Author is licensed under CC BY-SA
Notes: permit the flow of electricity in one direction, and block it in the other direction. Because of this, they can only be placed in a circuit in one direction. Light-Emitting Diodes (LED’s) are special types of diodes which emit light when current flows through them

## Slide 12: Resistors
Reduce current and voltage to components
Ohm Law: I=V/R
This Photo by Unknown Author is licensed under CC BY-SA
Notes: resist, but do not totally block, the flow of electricity. They are used to control the flow of current. Current can move either way through a resistor, so it doesn’t matter which way they’re connected in a circuit.

## Slide 13: Push Button
pushbuttons control the flow of current through a junction in a circuit

## Slide 14: Circuit Schematics
Circuit Schematic illustrate you how components are connected in a circuit.
For more info follow this link

## Slide 15: Electrical Flow
Components can be arranged in series/parallel
Current tends to follow the path of least resistance to the ground
In any given circuit, the total voltage around the path of the circuit is zero
The amount of current going into any point in a circuit is the same as the amount coming out of that point.

## Slide 16: Physical Computing with Rpi: GPIO
GPIO!

## Slide 17: Physical Computing with RPi: Build Circuit
Use GPIO Headers to create circuit
Write program to Read/Write to GPIO headers

## Slide 18: Physical Computing with RPi: GPIOZero
Python API for physical computing
Accessible and intuitive:
  Interfaces for common physical computing components

## Slide 19: GPIOZero
Multi paradigm (programming):
  Polling
  Blocking
  Callbacks
  Declarative

## Slide 20: GPIO: Supported Devices
LED (also PWM LED allowing change of brightness)
RGB LED
Buzzer
Motor
Button
Motion Sensor
Light Sensor
Analogue-to-Digital converters MCP3004 and MCP3008
https://gpiozero.readthedocs.io/en/stable/

## Slide 21: Physical Computing Lab: RPi Doorbell
Abstract Idea: Send email on button push event
Technologies:
  Button and Breadboard connected to GPIO
  PiCamera
  SMPT server/email service to send email
Use Case
  Button pushed
  PiCamera takes photo and stores on Rpi
  Image attached to email and sent using SMTP
  Recipient accesses image using mail client