## Slide 1: Wireless Network Protocols BLE
Dr. Frank Walsh
Dr. Kumar Yelamarthi

## Slide 2: Wireless Network Protocols & IoT
Vital enabler for Internet of Things
  Vast majority of IoT solutions will include one or more wireless technologies
Wireless enabled devices/wearables are a major reason for explosion in connected devices.
Global mobile network data traffic: End of 2020: 49 exabytes/month Forecast for 2026: 237 EB/month
1 EB = 1,000 petabytes (PB) = 1,000,000 terabytes (TB) = 1,000,000,000 gigabytes (GB)

## Slide 3: QI – the Electromagnetic Spectrum
This Photo by Unknown Author is licensed under CC BY-SA
https://imagine.gsfc.nasa.gov/science/toolbox/history_multiwavelength1.html
Notes: William Herschel was exploring the question of how much heat was contained by the different colours of visible light. He devised and experiment where he used a glass prism to separate sunlight into it's rainbow of colors. Then, he placed a thermometer under each color, with one extra thermometer just beyond the red light of the spectrum. He found that the thermometer that was seemingly out of the light had the highest temperature. Thus, he discovered infrared light.
James Clerk Maxwell equations developed a scientific theory to explain electromagnetic waves and successfully unified theories of light and electromagnetism, which is one of the great unifications in physics. Heinrich Hertz, a German physicist, applied Maxwell's theories to the production and reception of radio waves. The unit of frequency of a radio wave -- one cycle per second -- is named the hertz, in honor of Heinrich Hertz.

## Slide 4: Wireless Advantages
Look – no wires!
Mobility
Deployment
Productivity
Convenience
Notes: A Wireless LAN (WLAN) is a type of wireless network that is commonly used in homes, offices, and campus environments.
WLANs make mobility possible within the home and business environments.
Wireless infrastructures adapt to rapidly changing needs and technologies

## Slide 5: Problems
Physical differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different times
make communication across (even a point to point) wireless link “difficult” compared to wired link
Security
Speed
This Photo by Unknown Author is licensed under CC BY-NC-ND

## Slide 6: Wireless Networks Classification
Wireless technologies can be classified broadly according to network type:
We'll focus in these Areas
Notes:   Wireless Personal-Area Network (WPAN) – Low power and short-range (20-30ft or 6-9 meters). Based on IEEE 802.15 standard and 2.4 GHz frequency. Bluetooth and Zigbee are WPAN examples.
  Wireless LAN (WLAN) – Medium sized networks up to about 300 feet. Based on IEEE 802.11 standard and 2.4 or 5.0 GHz frequency.
  Wireless MAN (WMAN) – Large geographic area such as city or district. Uses specific licensed frequencies.
  Wireless WAN (WWAN) – Extensive geographic area for national or global communication. Uses specific licensed frequencies.

## Slide 7: Wireless Technologies
  WiFi - family of wireless network protocols, based on the IEEE 802.11 standards (1998)
  Bluetooth – IEEE WPAN standard used for device pairing up to 100m distance.
    Bluetooth Low Energy (BLE) – Supports mesh topology to large scale network devices.
    Bluetooth Basic Rate/Enhanced Rate (BR/EDR) – Supports point-to-point topologies and is optimized for audio streaming.
  WiMAX (Worldwide Interoperability for Microwave Access) – Alternative broadband wired internet connections. IEEE 802.16 WLAN standard for up 30 miles (50 km).
  Cellular Broadband – Carry both voice and data. Used by phones, automobiles, tablets, and laptops.
    Global System of Mobile (GSM) – Internationally recognized
    3G,4G,5G
    Satellite Broadband – Uses directional satellite dish aligned with satellite in geostationary orbit. Needs clear line of site. Typically used in rural locations where cable/DSL are unavailable.#
    Low Power Wide Area Networks(LPWAN), Narrowband (NB) IoT
    long-range communications at a low bandwith
    Sigfox, LORA, Vodafone NB-IoT
This Photo by Unknown Author is licensed under CC BY

## Slide 8: ISM Wireless Bands
A region of electromagnetic spectrum is reserved for use by Industrial, Scientific, and Medical (ISM) groups
These frequencies are not licensed to specific carriers
  are broadly available for products, and are used for LANs and PANs
Notes:   2.4 GHz (UHF) – 802.11b/g/n/ax
  5 GHz (SHF) – 802.11a/n/ac/ax

## Slide 9: 6 GHz Spectrum Allocation
Traditional ISM bands (2.4 GHz and 5 GHz) are crowded due to widespread use by Wi-Fi, Bluetooth, Zigbee, and other technologies.
In 2020: the FCC opened up a par of the 6 GHz range (5.925–7.125 GHz) for unlicensed use, enabling technologies like Wi-Fi 6E.
  EU has also adopted a similar change
Not officially part of ISM,
  New authorised unlicensed spectrum specifically for communication technologies like Wi-Fi
Advantages:
  Wider channels – higher speeds possible
  Low interference

## Slide 10: Wireless Technologies Comparison

## Slide 11: Bluetooth/BLE

## Slide 12: Personal Area Networks (PANs)
A PAN technology provides communication over a short distance
It is intended for use with devices that are owned and operated by a single user. For example
  between a wireless headset and a cell phone
  between a computer and a nearby wireless mouse or keyboard
Several standards
  Frequencies dedicated to Industrial, Scientific and Medical (ISM) band
  Bluetooth, Near Field Comms(NFC)

## Slide 13: Bluetooth
Used for short distance data exchanging, such as Personal Area Network
RF from 2.4 to 2.485 GHz
Originally invented by Ericsson (a telecom vendor) in 1994
Now managed by the Bluetooth Special Interest Group (SIG)
Frequency hopping spread spectrum (FHSS)
16000+ SIG member companies
Billions of products shipped
QI: The name "Bluetooth" comes from 10th century Danish king who united Danish tribes into a single kingdom.

## Slide 14: Bluetooth Classification

## Slide 15: Bluetooth “classic”
The “conventional” Bluetooth
Operates in 2.4GHz
Range: 1m - 100m (10m typical)
Connection-oriented: audio, file transfer, networking
Reasonably fast data rate: 2.1 Mbps
Power consumption:
  < Wifi < 3G,4G,5G

## Slide 16: Bluetooth Low Energy
"Bluetooth Smart“
Light-weight subset of classic Bluetooth
  Operates in same freq. Range, 2.4GHz
  introduced as part of the Bluetooth 4.0 core specification
Target Apps:
  Wireless battery-powered sensors eg. heart rate, thermometer, wearables
  Low bandwidth (you won't be streaming video)
  Not always on, constrained devices
All good for IoT devices!

## Slide 17: BLE vs Classic
Bluetooth and Bluetooth Low Energy are used for different purposes
Bluetooth Classic
  can handle a lot of data
  consumes battery quickly
BLE
  used for applications that do not need to exchange large amounts of data
  cheap
  Marginally further range

## Slide 18: BLE Roles
Broadcaster
  Transmitter only
Observer
  Receiver only
Peripheral(Slave)
Central(Master)
  Can take multiple connections
  Initiates connection to peripheral
One Device can have multiple roles
Broadcaster
Observer
Central
Peripheral
Peripheral
Peripheral
Notes: A device in the Broadcaster role transmits data to nearby devices without establishing a connection.Commonly used for applications like advertisements or beaconing (e.g., sending periodic messages about location or product information).
A device in the Observer role listens for broadcasted data from Broadcasters.It does not initiate or establish a connection. Smartphones scanning for nearby Bluetooth beacons.
A device in the Peripheral role advertises its availability for a connection and acts as a "slave" in the connection when a Central device connects to it.
A device in the Central role initiates connections with Peripherals and acts as the "master" in the connection.

## Slide 19: BLE Operation Modes
Peripheral and Central Devices ​
Master/central : will typically have more computing resources and available energy - a computer or a tablet, for example.​
Slave/peripheral : an embedded device - will be constrained in both computing resources and energy.​
Servers and Clients​
Server : the device that has information it wishes to share, and in BLE that is typically the peripheral (the embedded device).​
Client : the device that wants information and services, and in BLE that is typically the central device - the phone​

## Slide 20: BLE Connections
Initiating Connections
  The central is free to establish or terminate a connection
  The peripheral (the BLE device) cannot force the central to scan for BLE devices
The two modes BLE uses are:
  Advertising mode : the peripheral sends out Generic Access Profile (GAP) that any device in the area can pick up; this is how central devices know that there are peripherals around.
  Connected mode : the peripheral and a central device establish a one-to-one conversation. This is how they can exchange complex information.

## Slide 21: Advertising process
Operates in 2.4 GHz Band
Peripheral sets a specific advertising interval and transmit advertising packet
  longer delays saves power but less responsive
Transmits on all advertising channels in each interval(channel 37/38/39)
A listening device can optionally request the scan response payload,
  peripheral will respond with the additional data.
Advertising channels

## Slide 22: Connection Process
Initiated by central device in a specific response period
Central can issue connection request after receiving advertisement
Peripheral stops advertising after connection request (becomes a slave)
Slave waits for packets from Master.
  When received, connection established
Adv
37
Adv
38
Con
Req
Rx period

## Slide 23: Bluetooth LE Device Address
The Bluetooth Device Address is a 48-bit (6-byte) number uniquely identifies a device among peers.
  Similar to an Ethernet Media Access Control (MAC) address
Think of it as a unique address of a device
There are two types of device addresses and one or both can be set on a device:
  Random Address:
    Random number according to the Bluetooth SIG. Can be static(can only change on power cycle) or Private(resolvable/non-resolvable)
  Public Address:
    Calculated just like IEEE Ethernet LAN address

## Slide 24: BLE – Adaptive Frequency Hopping
Once Connected, Channel hopping pattern (from Server) used to minimise interference
AFH Disabled
AFH Enabled
Notes: Bluetooth Devices are radio frequency devices designed to use the 2.4 to 2.48 GHz frequency band known as the ISM band.
Bluetooth devices share this band with other devices
Frequency Hopping is a technique where when a link is formed the devices are synchronized to change channels together many times a second.
devices also use AFH, an adaptive form of frequency hopping by adapting the hop sequence to avoid channels in use by other devices operating in the same ISM band.

## Slide 25: GAP and GATT for BLE
Generic Access Profile (GAP) or Advertising
  Information advertised to central before connection
  Name of peripheral
  Is it connectable?
  Supported features (services)
Generic Attribute Profile (GATT)
  How to exchange data once connected
  Identifies Services, Characteristics and Descriptors
GAP
GATT
SMP
ATT
L2CAP
Link Layer
LE PHYSICAL

## Slide 26: Generic Access Profile (GAP)
GAP responsible for “device visibility.”
Determines how two devices can (or can't) interact with each other.
2 ways for a device to advertise with GAP
  Advertising Data payload
  Scan Response payload.
Advertising data payload is mandatory
Scan response payload is optional
  allows device designers to fit more information in the advertising payload such a strings for a device name, etc.

## Slide 27: Broadcast Network Topology
Some devices/apps only require advertise data.
  E.g. app requires peripheral to send data to more than one device at a time.
Can include small amount of custom data in 31 byte advertising or scan response payloads.
In this way, BLE peripheral can send data one-way to any devices in listening range
  BLE Beacons

## Slide 28: Bluetooth Connection
Establishing a connection between a peripheral and a central device results in 1 to 1 communication
  the advertising process will stop
  no longer be able to send advertising packets
Communication in both directions
Must use GATT services and characteristics to communicate

## Slide 29: GATT Services
Breaks data up into logic entities
Contains one or more characteristics
Each service distinguished by unique numeric ID called a UUID
  16 bit
Set of officially adopted BLE services can be seen on the Services
E.g. official Heart rate service
  service has a 16-bit UUID of 0x180D
  contains up to 3 characteristic
    Heart Rate Measurement, Body Sensor Location and Heart Rate Control Point.
Profile
Service 1
Characteristic
Service 2
Characteristic
Characteristic

## Slide 30: GATT Characteristics
Represents a single data point
Similarly to Services, each Characteristic distinguishes itself via a pre-defined UUID
  Also use standard characteristics defined by the Bluetooth SIG
E.G Heart Rate:
  the Heart Rate Measurement characteristic is mandatory for the Heart Rate Service
  Heart rate measurement has UUID of 0x2A37
If you write apps that use BLE, characteristics are what you will be after with your BLE peripheral

## Slide 31: BLE UUIDs
BLE characteristics are identified by 128-bit UUIDs, written as 32 hex digits in 5 groups: (xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxxxx).
All standard GATT types use the base: 0000xxxx-0000-1000-8000-00805f9b34fb.
The Heart Rate Measurement characteristic uses the 16-bit ID 0x2A37 defined by the Bluetooth SIG.
Substitution into the base UUID: The 16-bit value 0x2A37 is inserted into xxxx → 00002a37-0000-1000-8000-00805f9b34fb.
Standard vs custom characteristics: Standard characteristics (like HR) use this base+16-bit scheme; custom/vendor characteristics use arbitrary 128-bit UUIDs outside this base.

## Slide 32: GATT Transactions

## Slide 33: BLE Connected Network Topology
A peripheral can only be connected to one central device
Communication is 2 -way
Central device can be connected to multiple peripherals.
If data needs to be exchanged between two peripherals, a custom messaging system will need to be implemented
  all messages pass through the central device.

## Slide 34: What are beacons?
Low-cost, low-power transmitters equipped with Bluetooth Low Energy
Helps mobile devices detect proximity and determine micro-location

## Slide 35: BLE Beacons – How they work
Beacons don’t transmit content, they transmit a series of numbers
The transmitted signal allows another device to identify it and determine the device’s proximity to the beacon

## Slide 36: Beacons
Use Cases
  Proximity marketing
  Hyperlocal check-in
  Retargeting Ads
  Asset tracking
  Indoor navigation

## Slide 37: What is Eddystone?
BLE beacon broadcast standard developed by Google
Cross-platform and capable of supporting Android, iOS and any platform that supports BLE beacons

## Slide 38: Eddystone BLE Advertisement PDU

## Slide 39: What is iBeacon
Apple’s beacon standard
Android and iOS compatible, native only for iOS
Broadcasts one advertising packet and a unique ID
Beaconstac SDK can wake up Android apps, even if they are closed

## Slide 40: BLE Power consumption