## Slide 1: Single Board Computers
Frank Walsh
2023

## Slide 2: SBC vs μC
Single Board Computer (SBC)
  Example: Raspberry Pi
Microcontroller (μC)
  Example: Arduino Uno
What are they?
What are key differences?
This Photo by Unknown Author is licensed under CC BY-NC
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 3: What is a Single Board Computer(SBC)?
A complete computer on a single board
  CPU, RAM, storage, and I/O ports.
Runs a full-fledged operating system
  Linux distributions
Capable of multitasking, web browsing, and running software applications.
Examples:
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 4: Raspberry Pi
Low cost, single board computer
Linux OS
Same features as most laptops/workstations
USB Ports
RJ45 Ethernet
3.5mm audio
HDMI
LCD Display
Power
40 pin GPIO

## Slide 5: What is a Microcontroller?
A compact circuit designed for specific operations in embedded systems.
Contains a CPU, small RAM, storage, and operates without a full OS.
Executes pre-programmed tasks, ideal for hardware interactions.
Example:
  Automated Plant Watering System: An Arduino reads soil moisture levels and automatically waters a plant when it gets too dry.
This Photo by Unknown Author is licensed under CC BY-NC-ND
This Photo by Unknown Author is licensed under CC BY-NC

## Slide 6: Arduino wifi MKR1010
Powerful μC platform
IoT and network connectivity focused
  Good for networking modules!!!
Open source
Large online community
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 7: SBCs vs. Microcontrollers Key Differences
Power Consumption: Arduino is more energy-efficient than Raspberry Pi.
Complexity: Raspberry Pi can handle intricate tasks due to its robust CPU architecture, memory resources and OS.
Boot Time: Arduino starts nearly instantly, while Raspberry Pi requires boot-up time(like your laptop).
Cost: Microcontrollers are generally cheaper than SBCs.
Development: Raspberry Pi offers a typical Operating System and desktop-like environment, whereas Arduino requires external coding and uploading.

## Slide 8: SBCs vs. Microcontrollers Key Differences
Real-time:
  Microcontrollers are generally designed to perform specific tasks without the overhead of an operating system.
  Microcontrollers loop continuously waiting for input from sensor the react immediately.
  Real-time operation: can guarantee a task is executed in a predictable time frame.
    Can use “interrupt” handlers to achieve this. Triggered by a sensor input(e.g. tilt sensor in car)
  SBCs generally run full-fledged operating systems like Linux,
    can have varying response times due to task scheduling and other processes running in the background.
Microcontrollers can operate in Real-time, SBCs do not.

## Slide 9: Which one???
Task Simplicity:
  Use Arduino for simpler, hardware-focused tasks.
  Use Raspberry Pi for complex tasks or when a full OS is beneficial (e.g. image processing, DB I/O).
Power Constraints: For battery-operated or energy-efficient systems, Arduino is often a better choice.
Integration: Raspberry Pi is ideal for projects that need internet connectivity, computation & processing, or integration with complex software.
Budget: Consider cost implications, especially for large scale or commercial projects.

## Slide 10: Example Use Case1: ABS
Anti-lock Braking System (ABS)
  ABS is a safety anti-skid braking system that prevents the wheels from “locking up” during braking, which helps the driver maintain control.
How it works:
  Wheel Speed Sensors constantly measure the speed of each wheel and send this data to the ABS controller.
  ABS Controller processes the wheel speed data and determines if a wheel is about to lock up.
  If the ABS Controller detects a wheel is about to lock, it decreases the pressure to the brake until the wheel starts moving again.
Safety Critical System: Has to Work Always, Has to be Reliable, Has to be Fast, Can’t be waiting around for processor timeslot
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 11: Example Use Case1: ABS
The ABS controller needs to operate in real-time.
When a driver steps on the brake pedal, the ABS must instantly assess and react to wheel slip conditions to prevent skids
A delay in processing could reduce the effectiveness of the ABS, leading to potential accidents.
Microcontroller is the best option here and are used extensively in the automotive industry where safety, performance, and reliability are critical.(Incorporated into ECUs(electronic control units)

## Slide 12: Example Use Case2: Licence Plate Recognition (LPR)
LPR systems automate the process of identifying a vehicle's license plate to manage access, billing, security….
Capture: Cameras take pictures of vehicles' as they come and go.
Image Processing: The system processes these images to enhance clarity, adjust lighting, and prepare the image for plate extraction.
Plate Extraction: Program identify the rectangular region of the image containing the license plate.
Optical Character Recognition: The system then processes this extracted portion to recognise and read the characters on the license plate.
Database: The licence plate number is used to query/update a DB
This Photo by Unknown Author is licensed under CC BY-NC
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 13: Example Use Case2: Licence Plate Recognition (LPR)
A lot of computationally expensive processing here (image processing). May need a lot of CPU power and memory.
Short period to acquire, process and recognise licence plate is acceptable.
Quick, but not exact real-time processing, is OK.
Nobody will be hurt if it fails – not safety critical.
A networked/connected Single Board Computer connected to Camera is a viable option here.
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 14: Can you use both together?
Yep! If you want
Why?
  Microcontrollers are reliable, real-time and interface well with sensors (analog/digital sensors)
  OS on computer have a lot of processing power/software to work on data but can crash and have security vulnerabilities like any computer.
  Use Microcontroller to interface/control sensors and actuators
  Use SBC to process data/connect to other networks and services.