## Slide 1: Indirect Messaging
Frank Walsh

## Slide 2: Agenda
Indirect Messaging
  MQTT
  MQTT Security
Lab:
  Publish/Subscribe Telemetry data to broker.
  Publish/Subscribe Commands to Broker
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 3: Indirect Messaging
Publish Subscribe

## Slide 4: Using the “Middleman”
  Communication between processes using an intermediary
    Sender  “The middle-man”  Receiver
    No direct coupling
  Consider…
    What happens if a device fails during communication in Direct Coupling?
    What if you'd like to add
  Two important properties of intermediary in communication
    Space uncoupling (devices don't need to "know" about each other)
    Time uncoupling (devices don't need to be "available" at the same time)
A
B
A
B
Intermediary
Direct Communication
Indirect Communication

## Slide 5: MQTT
MQ Telemetry Transport (MQTT)
Telemetry
  Remote measurements
Created by IBM
  from message queueing (MQ) architecture used by IBM for service oriented networks.
  Telemetry data goes from devices to a server or broker.
  Uses a publish/subscribe mechanism.
Lightweight both in bandwidth and code footprint

## Slide 6: MQTT – publish subscribe
Topics/Subscriptions: Messages are published to topics.
  Clients can subscribe to a topic or a set of related topics
Publish/Subscribe: Clients can subscribe to topics or publish to topics.

## Slide 7: Publish Subscribe Process
A message is published once by a publisher.
Many things can receive the message.
The messaging service, or “broker”, provides decoupling between the producer and consumer(s)
A producer sends (publishes) a message (publication) on a topic (subject)
A consumer subscribes (makes a subscription) for messages on a topic (subject)
A message server / broker matches publications to subscriptions
  If no matches the message is discarded
  If one or more matches the message is delivered to each matching subscriber/consumer

## Slide 8: Publish-Subscribe Characteristics
A published messages may be retained
  A publisher can mark a message as “retained”
  The broker / server remembers the last known good message of a retained topic
  The broker / server gives the last known good message to new subscribers
A Subscription can be durable or non-durable
  Durable: messages forwarded to subscriber immediately, if subscriber not connected, message is stored and forwarded when connected
  Non-Durable: subscription only active when subscriber is connected to the server / broker

## Slide 9: MQTT Characteristics
MQTT protocol compresses to small number of bytes
  Smallest packet size 2 bytes
  Supports always-connected and sometimes connected
  Provides Session awareness
  “Last will and testament” enable applications to know when a client goes offline abnormally
  Typically utilises TCP-based networks.

## Slide 10: MQTT Characteristics
Three quality of service levels:
  0 = At most once (Best effort, No Ack),
  1 = At least once (Acked, retransmitted if ack not received),
  2 = Exactly once [Request to send (Publish), Clear-to-send(Pubrec), message (Pubrel), ack (Pubcomp)]
https://dzone.com/articles/internet-things-mqtt-quality

## Slide 11: MQTT Control Packets
The MQTT protocol uses MQTT Control Packets using the Control Header.
Control Packet consists of three parts:
  fixed header(present in all packets),
  variable header(optional)
  Payload(optional)
https://docs.devicewise.com/Content/Products/IoT_Portal_API_Reference_Guide/MQTT_Interface/MQTT-Control-Packets.htm

## Slide 12: MQTT Control Packets
MQTT Control Packet Types

## Slide 13: MQTT Last Will and Testament
Notify other clients about an ungraceful disconnected client.
Client can specify its last will message when it connects to a broker.
  normal MQTT message with a topic, retained message flag, QoS, and payload
  When an “ungraceful disconnect” occurs, the broker sends the last-will message to all subscribed clients of the last-will message topic.
https://www.hivemq.com/blog/mqtt-essentials-part-9-last-will-and-testament/

## Slide 14: MQTT is Open Source
Lots of implementations:
    Mosquitto
    Micro broker
    Really small message broker (RSMB): C
    Cloud broker services

## Slide 15: MQTT vs HTTP
Push delivery of messages / data / events
  MQTT – low latency push delivery of messages from client to server and server to client. Helps bring an event oriented architecture to the web
  HTTP – push from client to server but poll from server to client
Reliable delivery over fragile network
  MQTT will deliver message to QOS even across connection breaks
  Decoupling and publish subscribe – one to many delivery

## Slide 16: MQTT vs HTTP

## Slide 17
*sending and receiving 1024 messages of 1 byte each.(source: https://www.ibm.com/developerworks)

## Slide 18: Application Example
Home care monitoring solution
  Home and patient instrumented with sensors.
    E.g. door motion, blood pressure, pacemaker/defib.
  Collected by monitoring service (broker) using MQTT
  Subscribed by a health care service in the hospital
  Alerts relations/health care profs. if anything is out-of-order

## Slide 19: Code Example: Python