## Slide 1: IoT Platforms
Frank Walsh

## Slide 2: What are IoT platforms
IoT applications combine sensors, devices, data, analytics and integrations in a seamless and unified way
  e.g. your project!
IoT Platforms provide software tools and components to:
  connect sensors, devices, and data networks
  Analyse and store data
  Integrate with other apps
So what? We know the tech for that now (I2C, SPI, BLE, MQTT, Python...)
Main selling point of an IoT platform is software that it
  accelerates the IoT development process
  Focuses on IoT: brings in best of breed features
  Provides initial scaffolding for IoT projects

## Slide 3: What are IoT Platform
Many(not all) are cloud-based platforms that require subscription
Provide device/language agnostic set of Software Development kits
  Arduino/RPi/beagleboard
IoT development is generally iterative:
  Starts with initial simple use case
  Once operational, data/insights result in new usecased
IoT platforms should promote scalable, iterative development
  Allow for quick app development
  Ability to adapt/optimise apps quickly

## Slide 4: IoT Platform Characteristics
Manage many concurrent device connections
Connectivity across several connection types
"Off-the-peg" IoT protocol stack
Manage/analyse/visualise data
Integrations to other services/apps
App Development

## Slide 5: IoT Platform – general architecture
IoT Platform
Deploy algorithms to devices
Configure analytics/visuals/apps
Data/commands

## Slide 6: IoT Platform Advantages
Use sofware component that has been pre-built and pre-tested. This increases the reliability of your application and reduces development effort.
IoT frameworks constantly evolve, providing new features, integrations etc.
Encourages better "design pattern" for your IoT app.
Predefined APIs and docs
  Great for collaboration
"Baked-in" standards and features:
  Security, authentication, scalability...

## Slide 7: Which one?
Connectivity
  Does the platform provide suitable capability and integrations (WiFi/Cellular/LPWan-Sigfox)
Maturity
  In business for long? Critical mass in developer community?
Free
  Is there a free tier (handy for evaluation)?
Service type
  Platforms try to distinguish themselves – what specialisms/USP does it have?
Security
  What security model do they use? Is there security issues reported in past?
Geographic area
  Does it operate well at your location (can you select edges/data centres)

## Slide 8: Examples:

## Slide 9: Mobile Device IoT using Blynk
Frank Walsh

## Slide 10: Mobile Devices and IoT
Critical component of many IoT solutions is the mobile phone/tablet.
  IOS/Android dominate
>2.6 billion users worldwide
  Simple, mobile connection to the internet
Provides nice features for IoT apps
  Packed with sensors (Location, accelerometer, camera)
  Can connect/interlink other smart devices using Bluetooth, BLE, etc.

## Slide 11: Mobile Apps in IoT, Examples
Wearables
  wristwatches, eyeglasses and rings
Healthcare
  Medical sensors obtain health data and transfer to a mobile app.
  This data can be transferred remotely to doctor/ family members
SmartHome
  Nest – see who’s at the door...
AgriTech
  MooCall

## Slide 13: What's Blynk
Yet Another IoT Platform
  Specialism: mobile application builder
"Blynk is a full suite of software required to prototype, deploy, and remotely manage connected electronic devices at any scale: from personal IoT projects to millions of commercial connected products."

## Slide 14: Platform Overview
4 Compnents
  Blink.Cloud
  Blynk.App
  Blynk.Console
  Blynk.Edgent (Device Libraries)

## Slide 15: Blynk.Console
Blynk.Console is a feature-rich web application
Register with Blynk to gain access
Use it to:
  Configuration of how connected devices work on the platform + application settings.
  Management of devices, their data, users, organizations and locations
  Remote monitoring and control of devices

## Slide 16: Blynk App
Blynk App is a multi-functional native iOS and Android mobile application
Use it to:
  Remote monitoring and control of connected devices that work with Blynk platform
  Configuration of mobile UI during prototyping and production stages
  Automate work of connected devices
Allows you to create mobile applications using drag and drop
  Uses "widgets"
No Code!!!
  Don't worry – that comes later

## Slide 17: Blynk Library
Lightweight embedded library that runs on over 400 supported hardware models
  We’ll use a unsupported python one
Use it to:
  bring your device online and authenticating)
  Connectivity management (WiFi, Cellular, Ethernet)
  Data transfer Over-the-air firmware updates (for selected hardware models)
Available for most popular hardware platforms
  RPi, Arduino, ...
Enable communication between the device and cloud API to work with specific Blynk App and Blynk cloud features
Python, Javascript, C++ … on the RPi.

## Slide 18: Blynk cloud Platform
Blynk Cloud is a server infrastructure – heart of Blynk IoT platform. Cloud is responsible for binding all the platform components together.
Controls all the communications between the mobile device(e.g. your phone) and hardware (e.g. the RPi)
Remember we talked about the benefits of indirect communication.
It's Cloud-based but you can run your own private Blynk Server
A bit like MQTT...(actually, after peeking at the source code, it uses the same MQTT libraries from the previous lab!)

## Slide 19: Benefits
Don’t need to be a mobile app developer
Minimal code
Reasonably mature (around since 2014)
Very quick to create a prototype
If you want, process to publish to App store/Google Play
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 20: Features
Similar API & UI for all supported hardware & devices
Connections/ Protocols:
WiFi
Bluetooth and BLE
Ethernet
USB (Serial)
GSM
…
Set of easy-to-use Widgets
Connect device with no code writing
Easy to integrate and add new functionality using virtual pins
History data monitoring via SuperChart widget
Device-to-Device communication using Bridge Widget
Sending emails, tweets, push notifications,

## Slide 22: Blynk Concepts
Devices
Templates
Events
Dashboards

## Slide 23: Blynk Concepts: Device
A “device” can be:
  A small MicroController based hardware (e.g. Arduino, Raspberry Pi, etc)
  A finished physical product like a Smart Air Conditioner, or a virtual service that sends data to Blynk Cloud using REST API.
Each device has an “Authentication Token”. This is a unique identifier generated in Blynk.Cloud
Every device uses a Device Template.

## Slide 24: Blynk Concepts: Device Template
A Device Template is a set of configurations used by similar devices.
A device template specifies:
  General Settings: general settings of the device(name, ID etc..)
  Metadata: Serial Number field, email field to use for email notifications
  Datastreams: channels for any data that flows in and out from the device to the cloud. For example sensor data should go through a Datastream. These are also known as “Virtual Pins”.
  Events: important events in the life of the device that should be logged and, if needed, used for notifications. Events can be triggered from the device itself or externally using HTTP API
  Dashboards: Set of UI elements to visualise data and send commands/data to/from device
    There are two dashboards: Web and Mobile

## Slide 25: Blynk Concepts: Web Dashboard
a set of UI elements (widgets) to visualize the data from the device accessible for the users in Blynk.Console – a web-based application.

## Slide 26: Blynk Concepts: Mobile Dashboard
a set of UI elements (widgets) to visualize the data in Blynk mobile apps for iOS and Android.
Mobile apps also contain a template of how device is represented in the list of devices (tiles)

## Slide 27: Development Steps
Create an Account with Blynk
Add a Device
  Choose your hardware
  Create “Template”
  This will result in an Authentication Credentials for that Device
Code the Hardware Device(e.g. Rpi) Use the relevant library(e.g. Python Library)
Install Blynk App on Phone
  Develop Blynk

## Slide 28: Add a Device
Create a new device
Set Notifications:
  Specify who gets notifications, which events will trigger notifications, and which channel should be used.
  3 options:
    E-mail
    Push notifications - a push notification is a message that pops up on a mobile device. Users don't have to be in the app to get them
    SMS - notification will be delivered as a text message using mobile operator (only available in paid option though…)

## Slide 29: Working with Templates
Datastreams is a way to structure data that regularly flows in an out from device.
Use it for sensor data, any telemetry, or actuators.
Virtual Pin is a concept invented to provide exchange of any data between hardware, web and mobile app.
Virtual pins allow you to interface with any sensor, any library, any actuator.Think about Virtual Pins as a box where you can put any value, and everyone who has access to this box can see this value.
You can set UNITS that will be viewed in the Widget by selecting them from the dropdown menu.
It's a very powerful feature to display and send any data from your hardware to the application.Please make sure you differentiate Virtual Pins from physical GPIO pins on your hardware.

## Slide 30: Working with Templates: Events
Events are used to track important events happening on your devices.
Events can trigger notifications which can be
  sent over email
  delivered as push notifications to user’s phone
  SMS
Examples:
  log a moment when a temperature reached a certain threshold and send a notification to selected users
  You need to log a total working hours of the device. If it approaches or goes beyond a max value, you would need to notify technical support so that they can replace the device

## Slide 31: Blynk.Apps
Using the Blynk App, a Mobile Dashboard can be built from Widgets - modular UI elements which can be positioned on the canvas.
To add Widgets to Canvas:
  tap anywhere on empty canvas or press PLUS icon in the top right corner of the app.
  A Widget Box will open
  Find the widget you need and tap on it
  Widget will placed in the first empty area required for this widget
  Configure Widget.

## Slide 32: Widgets
Categorised as:
  Controllers
  Display
  Notifications
  Interface
    Tabs, Menu, Map..

## Slide 33: Example
DEMO!!!!!

## Slide 34: Python Features: Decorators
A decorator is a function that:
  Associated with function
  Adds extra behaviour
Example in Flask: @app.route("/")
It tells Flask: “When someone visits /, call the home() function.”
It wraps home() with logic that:
  Matches URLs
  Handles HTTP requests/responses
  You write only the core logic (return "Hello, world!"),the decorator takes care of all the web-server plumbing.
Also used in Event Driven programming to match events to functions
  as you’ll see using BlynkLib

## Slide 35: Python Features: Datetime module
A built-in Python module for working with dates and times
Parse, format, and display dates
Do date arithmetic (e.g., 5 days from now)
Handle timestamps, scheduling, logging, time differences

## Slide 36: Python Features: Error Handling
A way to elegantly catch and manage problems that happen while your program runs.
Can be used to prevent your program from crashing.
Uses try, except, else, and finally blocks.
Use it to:
  Handle expected issues (files missing, bad input, network errors)
  Give clearer error messages
  Keep your program running safely
  Clean up resources (files, network connections)

## Slide 37: Python Features: Error Handling (and Dates!)
Try to run this code, but be ready to catch errors
If an exception (error) of the type you specify happens (here: ValueError), it jumps out of the try block and into the matching except block.

## Slide 38: WARNING!!!!
Blynk has gone very commercial
Still has “free tier” but just 200,000 messages allowed
You can burn through that very quickly if you’re not careful
My approach:
  Just send messages when you need to
  Stop the app immediately on finishing testing